Crooke’s Tube (5H30.15)

Location: 29-6R

Concept/Purpose: Force on Moving Charges

Procedure/Explanation: The Crooke’s tube is similar to a CRT except there is no phosphor screen at the end of the tube. Instead, the phosphor screen is along the side of the tube so the entire beam path can be seen. A small bar magnet is used to deflect the beam at various places to show the resultant path of the electrons in a magnetic field.