Oersted Apparatus (5H10.20)

Location: 29-Top

Concept/Purpose: Magnetic Fields

Procedure/Explanation: A large copper tube is mounted on a piece of wood. A low voltage, high current power supply is wired to the tube via a small switch.  A large compass is placed just below the tube and deflects in the direction of the magnetic field when the switch is pressed.  The switch should not be pressed for more than 5-10 seconds to avoid burning the wires.