Tipping Clown (1J11.15)

Location: 54-4R

Concept/Purpose: Exceeding Center of Gravity

Procedure/Explanation: The clown is a large board with a clown face painted on the front. Mounted on the bottom of the board are two pieces of 2x4 representing the clown’s feet. The 2x4’s are mounted such that they can be pivoted to create a wide or narrow base. They also allow the clown to be tilted from side to side. Pinned to the middle of the board is a piece of sheet metal that acts as the clown’s tie. As the clown is tilted from side to side his tie pivots to create a perpendicular line between the ground and his center of mass. If his tie points outside his feet (essentially his base) the clown falls over and if his tie points inside his feet he can remain standing on his own.